## Slide 1: How to Program an HT with Chirp
By Patrick Hall
KO4HEX

## Slide 2: Navigate to Chirp webpage:
Go to Google.com
Search Chirp
Find the chirp.danplanet.com link

## Slide 3: Select “get it!”

## Slide 5
Navigate to your downloads and follow the prompts to install

## Slide 7: File - New:
This is opening a new “file”
For the purpose of this presentation, I will leave it as “Untitled.csv”
I will also remove the information in the first row that auto populated as 146.01 as this is not needed.
We will customize this file to upload to the radio

## Slide 8: Radio - Download From Radio
Hook up your radio to a computer with a program cable
Find the correct port
Select your “vendor”
Select your radio then click “ok”
This will put any information from your radio on to the computer in the file that you can edit

## Slide 9: Radio – Query Source – Repeater Book
This will query the repeaterbook website and download the repeaters based on what you put in this query.
It is an easy way to “mass download” repeaters to not input them manually.

## Slide 10: RepeaterBook Query
Results from the previous Query

## Slide 11: Copy the repeaters you want with Ctrl Click, Then paste in new tab “untitled.csv”
You may use Ctrl click to select individual rows or Shift click to select a range of rows
You can also combine Shift click and Ctrl click – just be careful to use the right one in the right situation or you will end up selecting thing you don’t want
Copy either Ctrl +C or right click and “Copy”

## Slide 12: View of “untitled.csv” after pasting selected repeaters from previous slide
Note: I did remove the first entry 146.01 from the “untitled.csv” file before I pasted these entries in.

## Slide 13: File – Open Stock Config – US NOAA Weather
Importing NOAA WX then copying the stations

## Slide 14: Updated file(Untitled.csv)with NOAA, and Proxy Search

## Slide 15: Right click cell – properties – edit cell
You can select multiple channels at once. I did this for the next slide.
This will allow you to edit several fields at once for multiple rows
This is also where you can manually enter in repeaters

## Slide 16: Tip: selected multiple WX rows to turn Duplex OFF. This prevents transmit on unwanted channels

## Slide 17: Upload to Radio!
Plug your radio into the computer with the programming cable
Turn your radio on
Go to Radio-Upload to Radio
Get on the Air!!